## Slide 1
Virtual (VRT) Geospatial Format
Tim Cera, P.E.

## Slide 2: What is a VRT?
Developed by Open Source Geospatial Foundation
Part of GDAL/OGR
eXtensible Markup Language
  Describes transformation from a source dataset
File extension is “.vrt”
Raster transformations
Vector transformations

## Slide 3: Why VRT?
Space efficient
  Many very small VRTs can transform the same source, without copying
Up-to-date
  Transformations are performed in memory when the VRT is opened, so uses up-to-date information in the source data

## Slide 4: VRT Transformations
Transformation | Raster | Vector
Reprojection | X | X
Mosaic | X | X
Look up table (LUT) | X | 
Structured Query Language (SQL) |  | X

## Slide 5: Post-Processing
Develop PERLND ID raster
  National Land Cover Database (NLCD) 30x30 meter
  Subwatershed raster
Develop Look Up Table (LUT)
  hspfbintoolbox to develop PERLND ID to model output (LUT)
Zonal statistics to get average across MODFLOW cell

## Slide 6: Create Raster of PERLND Labels
HSPF PERLND labels 1-999
PERLND label = RCHRES * 20 + HSPF Land Cover
RCHRES | Water PERLND | Developed Open Space PERLND | ... | Wetland PERLND
1 | 21 | 22 | ... | 32
2 | 41 | 42 | ... | 52
3 | 61 | 62 | ... | 72
... | ... | ... | ... | ...

## Slide 7: VRT Raster Look Up Table (LUT)
<VRTDataset rasterXSize="3554" rasterYSize="6318">
<SRS>PROJCS["NAD83(HARN) / Florida GDL Albers",GEOGCS["NAD83(HARN)",DATUM["NAD83_High_Accuracy_Reference_Network",SPHEROID["GRS 1980",6378137,298.257222101,AUTHORITY["EPSG","7019"]],TOWGS84[0,0,0,0,0,0,0],AUTHORITY["EPSG","6152"]],PRIMEM["Greenwich",0,AUTHORITY["EPSG","8901"]],UNIT["degree",0.0174532925199433,AUTHORITY["EPSG","9122"]],AUTHORITY["EPSG","4152"]],PROJECTION["Albers_Conic_Equal_Area"],PARAMETER["standard_parallel_1",24],PARAMETER["standard_parallel_2",31.5],PARAMETER["latitude_of_center",24],PARAMETER["longitude_of_center",-84],PARAMETER["false_easting",400000],PARAMETER["false_northing",0],UNIT["metre",1,AUTHORITY["EPSG","9001"]],AXIS["X",EAST],AXIS["Y",NORTH],AUTHORITY["EPSG","3087"]]</SRS>
<GeoTransform> 5.3594982359709428e+05, 3.0000448581084310e+01, 0.0000000000000000e+00, 6.4710220398997108e+05, 0.0000000000000000e+00, -3.0000448581084310e+01</GeoTransform>
<VRTRasterBand dataType="Int16" band="1">
<NoDataValue>-9999</NoDataValue>
<ComplexSource>
<SourceFilename relativeToVRT="1"> wgrid.tif </SourceFilename>
<SourceBand>1</SourceBand>
<SourceProperties RasterXSize="3554" RasterYSize="6318" DataType="Byte" BlockXSize="256" BlockYSize="256" />
<SrcRect xOff="0" yOff="0" xSize="3554" ySize="6318" />
<DstRect xOff="0" yOff="0" xSize="3554" ySize="6318" />
<NODATA>0</NODATA>
<LUT>
1:20,2:40,3:60,4:80,5:100,6:120,7:140,8:160,9:180,10:200,11:220,12:240,13:260,14:280,15:300,16:320,17:340,18:360,19:380,20:400,21:420,22:440,23:460,24:480,25:500,26:520,27:540,28:560,29:580,30:600,31:620,32:640,33:660,34:680,35:700,36:720,37:740,38:760,39:780,40:800,41:820,42:840,43:860,44:880,45:900,46:920,47:940,48:960
</LUT>
</ComplexSource>
</VRTRasterBand>
</VRTDataset>
wgrid.tif
baselue.vrt

## Slide 8: VRT Raster Look Up Table (LUT)
<VRTDataset rasterXSize="3554" rasterYSize="6318">
<SRS>PROJCS["NAD83(HARN) / Florida GDL Albers",GEOGCS["NAD83(HARN)",DATUM["NAD83_High_Accuracy_Reference_Network",SPHEROID["GRS 1980",6378137,298.257222101,AUTHORITY["EPSG","7019"]],TOWGS84[0,0,0,0,0,0,0],AUTHORITY["EPSG","6152"]],PRIMEM["Greenwich",0,AUTHORITY["EPSG","8901"]],UNIT["degree",0.0174532925199433,AUTHORITY["EPSG","9122"]],AUTHORITY["EPSG","4152"]],PROJECTION["Albers_Conic_Equal_Area"],PARAMETER["standard_parallel_1",24],PARAMETER["standard_parallel_2",31.5],PARAMETER["latitude_of_center",24],PARAMETER["longitude_of_center",-84],PARAMETER["false_easting",400000],PARAMETER["false_northing",0],UNIT["metre",1,AUTHORITY["EPSG","9001"]],AXIS["X",EAST],AXIS["Y",NORTH],AUTHORITY["EPSG","3087"]]</SRS>
<GeoTransform> 5.3594982359709428e+05, 3.0000448581084310e+01, 0.0000000000000000e+00, 6.4710220398997108e+05, 0.0000000000000000e+00, -3.0000448581084310e+01</GeoTransform>
<VRTRasterBand dataType="Int16" band="1">
<NoDataValue>-9999</NoDataValue>
<ComplexSource>
<SourceFilename relativeToVRT="1">
NLCD/NLCD.tif
</SourceFilename>
<SourceBand>1</SourceBand>
<SourceProperties RasterXSize="3554" RasterYSize="6318" DataType="Byte" BlockXSize="3554" BlockYSize="2" />
<SrcRect xOff="0" yOff="0" xSize="3554" ySize="6318" />
<DstRect xOff="0" yOff="0" xSize="3554" ySize="6318" />
<NODATA>0</NODATA>
<LUT>
11:1,12:1,21:2,22:3,23:4,24:5,31:6,41:7,42:7,43:7,52:8,71:9,81:10,82:11,90:12,95:12
</LUT>
</ComplexSource>
</VRTRasterBand>
</VRTDataset>
NLCD.tif
hspflue.vrt

## Slide 9: VRT Raster Look Up Table (LUT)
baselue.vrt
hspflue.vrt

## Slide 10: PERLND Raster
gdal_calc.py
-A baselue.vrt
-B hspf_lc.vrt
--calc=A+B
--outfile=lue.tif
--NoDataValue=-9999
--type=Int16
--co COMPRESS=DEFLATE
--co PREDICTOR=2
--co TILED=YES
--overwrite

## Slide 11: hspfbintoolbox
hspfbintoolbox extracts results from HSPF binary files
Python, cross-platform tool
Command line and Python library
Installation (typical):
  pip install hspfbintoolbox
Used to create Look Up Tables for nearly all HSPF variables, yearly, and monthly

## Slide 12: VRT Raster Look Up Table (LUT)
<VRTDataset rasterXSize="3554" rasterYSize="6318">
<SRS>PROJCS["NAD83(HARN) / Florida GDL Albers",GEOGCS["NAD83(HARN)",DATUM["NAD83_High_Accuracy_Reference_Network",SPHEROID["GRS 1980",6378137,298.257222101,AUTHORITY["EPSG","7019"]],TOWGS84[0,0,0,0,0,0,0],AUTHORITY["EPSG","6152"]],PRIMEM["Greenwich",0,AUTHORITY["EPSG","8901"]],UNIT["degree",0.0174532925199433,AUTHORITY["EPSG","9122"]],AUTHORITY["EPSG","4152"]],PROJECTION["Albers_Conic_Equal_Area"],PARAMETER["standard_parallel_1",24],PARAMETER["standard_parallel_2",31.5],PARAMETER["latitude_of_center",24],PARAMETER["longitude_of_center",-84],PARAMETER["false_easting",400000],PARAMETER["false_northing",0],UNIT["metre",1,AUTHORITY["EPSG","9001"]],AXIS["X",EAST],AXIS["Y",NORTH],AUTHORITY["EPSG","3087"]]</SRS>
<GeoTransform> 5.3594982359709428e+05, 3.0000448581084310e+01, 0.0000000000000000e+00, 6.4710220398997108e+05, 0.0000000000000000e+00, -3.0000448581084310e+01</GeoTransform>
<VRTRasterBand
dataType="Float32" band="1">
<NoDataValue>-9999</NoDataValue>
<ComplexSource>
<SourceFilename relativeToVRT="1">
../gis/lue_irr.tif
</SourceFilename>
<SourceBand>1</SourceBand>
<SourceProperties RasterXSize="3554" RasterYSize="6318" DataType="UInt16" BlockXSize="256" BlockYSize="256" />
<SrcRect xOff="0" yOff="0" xSize="3554" ySize="6318" />
<DstRect xOff="0" yOff="0" xSize="3554" ySize="6318" />
<NODATA>0</NODATA>
<LUT>
401:1.9615,402:5.9667,403:40.548,404:36.128,406:7.9741,407:3.7158,408:4.9182,409:4.915,410:5.4634,411:4.4458,412:3.3966,417:6.3115,418:5.0476,421:
</LUT>
</ComplexSource>
</VRTRasterBand>
</VRTDataset>
agwi_2001.vrt
lue_irr.tif

## Slide 13: VRT to Mosaic
Need seamless raster layer to use zonal statistics
VRT can be used to mosaic
  Other VRTs!
GDAL command line utility:
  gdalbuildvrt out.vrt in01.vrt in02.vrt…

## Slide 14: Zonalstats
Used Python library ‘rasterstats’
http://pythonhosted.org/rasterstats/

## Slide 15: SQL Vector Selection by Attributes
<OGRVRTDataSource> <OGRVRTLayer name="03080101_clip"> <SrcDataSource>
WBD_HUC8.shp
</SrcDataSource> <SrcSQL> SELECT * FROM WBD_HUC8 WHERE HUC_8 = '03080101' </SrcSQL> </OGRVRTLayer> </OGRVRTDataSource>
03080101_clip.vrt
WBD_HUC8.shp

## Slide 16: SQL Vector Selection by Attributes
<OGRVRTDataSource>
<OGRVRTLayer name="03080101_area_m2">
<SrcDataSource>
WBD_HUC8.shp
</SrcDataSource>
<SrcSQL>
SELECT ACRES*4046.8726
AS AREA_M2
FROM WBD_HUC8
</SrcSQL>
</OGRVRTLayer>
</OGRVRTDataSource>
03080101_area_m2.vrt
WBD_HUC8.shp

## Slide 17: SQL Vector Attribute Calculations
<OGRVRTDataSource>
<OGRVRTLayer name="03080101_area_m2">
<SrcDataSource>
WBD_HUC8.shp
</SrcDataSource>
<SrcSQL>
SELECT ACRES*4046.8726
AS AREA_M2
FROM WBD_HUC8
</SrcSQL>
</OGRVRTLayer>
</OGRVRTDataSource>
03080101_area_m2.vrt
WBD_HUC8.shp

## Slide 18: SQL Vector Geometry Calculatiions
<OGRVRTDataSource>
<OGRVRTLayer name="03080101_geo">
<SrcDataSource>
WBD_HUC8.shp
</SrcDataSource>
<SrcSQL dialect="SQLITE">
SELECT
*,ST_Area(GEOMETRY)*0.0002471
AS Area_ac
FROM WBD_HUC8
</SrcSQL>
</OGRVRTLayer>
</OGRVRTDataSource>
03080101_geo.vrt
WBD_HUC8.shp

## Slide 19: SQL Vector Geometry Union
<OGRVRTDataSource>
<OGRVRTLayer name="03080101_geo1">
<SrcDataSource>
WBD_HUC8.shp
</SrcDataSource>
<SrcSQL dialect="SQLITE">
SELECT ST_Union(GEOMETRY)
FROM WBD_HUC8
WHERE HUC_8
LIKE '0308010%'
</SrcSQL>
</OGRVRTLayer>
</OGRVRTDataSource>
03080101_geo1.vrt
WBD_HUC8.shp

## Slide 20: SQL Vector CSV Files
<OGRVRTDataSource>
<OGRVRTLayer name="water_level_station_list">
<SrcDataSource relativeToVRT=1>
water_level_station_list.csv
</SrcDataSource>
<GeometryType>
WkbPoint
</GeometryType>
<LayerSRS>WGS84</LayerSRS>
<GeometryField
encoding="PointFromColumns"
x="Longitude"
y="Latitude"/>
</OGRVRTLayer>
</OGRVRTDataSource>
water_level_station_list.vrt
water_level_station_list.csv
water_level_station_list.csvt
SiteName SiteCode Latitude Longitude
10B LATERAL 405 AB S-405 NEAR VINELAND, FLA NWISDV:02266293 28.39472948 -81.5844349
10B LATERAL 405 BL S-405 NEAR VINELAND FLA NWISDV:02266294 28.3945628 -81.5843794
10B REEDY CREEK BELOW S-46 NR VINELAND FLA NWISDV:02266026 28.40417345 -81.61146309
...
String,String,Real,Real